## Slide 1: Tiny Circuit Hacks: Too Many LEDs!
Paul H. Dietz, PhD
Distinguished Engineer in Residence
Department of Computer Science
University of Toronto
October 2024

## Slide 2: Prerequisites
Played with Arduino before
  Made an LED blink on and off
An understanding of voltage and current
Slides are at: https://github.com/paulhdietz/TooManyLEDs

## Slide 3: Ideal Diode Model
No current flows until voltage reaches (forward voltage)
Above , acts like a short so generally need some way to limit the current
I
V

## Slide 4: Powering an LED
Need to limit the current
  Typically use a resistor
Example:
  =1.5V
  R=220
  I = (5V-1.5V)/220  15.9mA

## Slide 5: Digital I/O Pins Ideal Model

## Slide 6: 3 Ways of Controlling an LED From A Micro

## Slide 7: 2 LEDs, 2 Pins
An LED only lets current flow one direction
Flip high and low to change which LED lights
Fundamental Limitation: can only light one LED at a time!
Solution: Multiplexing (Scanning)
  Can only be half as bright
  Increase current to compensate?

## Slide 8: Bidirectional LEDs on Each Pin
Two LEDs for each additional pin
Unused Pins are set to Input - Disconnected
This is starting to be a significant win
  n Pins, 2(n-1) LEDs

## Slide 9: Row-Column
X+Y Pins, X*Y LEDs
  An entire row can be controlled simultaneously
  Often used for driving 7-segment displays where digits are driven one at a time

## Slide 10: Seven Segment Display
“Seven” segment displays can be common anode or common cathode
Digit drive needs to handle more current, so an external transistor is often utilized
Source: https://www.jameco.com/Jameco/workshop/TechTip/working-with-seven-segment-displays.html

## Slide 11: Bidirectional Row-Column
X+Y Pins, 2*X*Y LEDs
Basically, a matrix form of the bidirectional drive
Can’t address a row at a time – single LED mutliplexing

## Slide 12: Bidirectional Between EVERY Pair: Charlieplexing
n Pins, n2 - n pairs of Pins
To drive, turn one pin high, one low, other Input
Note path is through 2R

## Slide 13: Another Loop?
There is a parasitic path through other LEDs, but with two LEDs in series
  It will not turn on unless the forward voltage of drop of those two LEDs is less than the forward voltage drop of the desired LED

## Slide 14: Charlieplexing Matrix
A matrix with the same wires on for the rows and columns, missing the diagonal

## Slide 15: Charlieplexing Layouts
Source: https://en.wikipedia.org/wiki/Charlieplexing

## Slide 16
Chart: Number of Pins vs. Number of LEDs
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
One per Pin | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Bidirectional | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18
Row-Col | 1 | 2 | 4 | 6 | 9 | 12 | 16 | 20 | 25
Bi Row-Col | 2 | 4 | 8 | 12 | 18 | 24 | 32 | 40 | 50
Charlieplex | 2 | 6 | 12 | 20 | 30 | 42 | 56 | 72 | 90

## Slide 17: Can YOU Do Better?
Theoretically, YES
  If each pin has 3 states (HIGH, LOW, INPUT) you should theoretically be able to address 3n – 1 LEDs with n pins
Practically, YES
  You can add extra electronics so you can send a sequence of data to control large numbers of LEDs

## Slide 18: LEDs with Built-In Controllers
Different color LEDs in single package with a controller (e.g. WS2812B, AdaFruit NeoPixel, etc.)
Simple serial data protocol, designed to be daisy chained
Source: https://amptech.co.nz/WS2812B-LED-String-with-Arduino

## Slide 19: Data Protocol
Specifics depend on controller chip
  Controller grabs the first hunk of data to control its LEDs, and passes on the rest
    LEDs are effectively “addressed” by how far they are from the first
  Unusual “0” and “1” timing
    Not straightforward to use standard communications peripherals
  Bit rate often in excess of 1Mbps
    Requires low level bit banging, with precise timing
      Libraries typically hand-written in assembly
Source: https://lastminuteengineers.com/ws2812b-arduino-tutorial/

## Slide 20: Cost Comparison
As of October 6, 2024, JLCPCB Parts Library
RGB with controller: Xinglight XL-5050RGBC-WS2812B-S
  Quantity 1: US$0.0262 each
  Quantity 5000: US$0.0158 each
Basic red LED: Yongyu Photoelectric SZYY0603R1
  Quantity 1: US$0.0027 each
  Quantity 4000: US$0.0023 each
Source: JLCPCB

## Slide 21: Which to Use?
A couple of LEDs
  Wire directly to pins
A multi-digit 7-segment display, CC or CA
  Row-column with scanned digits
Show state where one of many LEDs is on
  Charlieplexing is ideal because allows full brightness on single LED
Cheap, little display (e.g. Arduino UNO R4 WiFi)
  Charlieplexing lots of discrete LEDs is cheap
A long, colorful, light strip for room lighting
  RGB LEDs with built-in controllers, e.g. WS2812B
Sources: https://www.first-components.com/it/display-solutions-led-display, https://store-usa.arduino.cc/products/uno-r4-wifi, https://www.dfrobot.com/product-1113.html